Generic Assumptions

Thermal Unit Commitment

2008 SSG-WI Base Case

TSG Meeting

July 13, 2005

- “Buckets” were agreed on by SSG-WI to classify units by fuel, technology, size, and vintage.  The buckets were developed for purposes of creating generic heat rate curve and other assumptions necessary for GridView’s thermal unit commitment logic.  The buckets recognize significant differences in heat rate curves and other operating characteristics between thermal units in the West.

| Bucket | Fuel | Technology | Size | Vintage |
| --- | --- | --- | --- | --- |
| 1 | Gas/Oil | Steam | <100 MW | <1960 |
| 2 | Gas/Oil | Steam | >=100 MW | <1960 |
| 3 | Gas/Oil | Steam | <100 MW | >=1960 |
| 4 | Gas/Oil | Steam | >=100 MW | >=1960 |
| 5 | Gas | SCCT |  | <1985 |
| 6 | Gas | CCCT |  | <1985 |
| 7 | Gas | SCCT | <70 MW | >=1985 & <2006 |
| 8 | Gas | SCCT | >=70 MW | >=1985 & <2006 |
| 9 | Gas | CCCT |  | >=1985 & <2001 |
| 10 | Gas/Oil | CCCT- Frame F |  | >=2001 |
| 11 | Gas | DT |  | <1985 |
| 12 | Gas | DT |  | >=1985 |
| 13 | Gas | SynCrude/Canadian Tar Sands |  |  |
| 14 | OIL | IC |  |  |
| 15 | OIL | SCCT |  |  |
| 16 | Coal | Steam | <100 MW | <1960 |
| 17 | Coal | Steam | >=100 MW | <1960 |
| 18 | Coal | Steam | <100 MW | >=1960 |
| 19 | Coal | Steam | >=100 MW | >=1960 |
| 20 | Bio/WH/Ref/Wood | Steam |  |  |
| 21 | GEO | GE |  |  |
| 22 | URAN | NUCLEAR |  |  |
| 23 | SUN | SL |  |  |
| 24 | PC | Steam |  |  |
| 25 | Gas | SCCT |  | >=2006 |
| 26 | Gas/Oil | CCCT- Frame G | >450 MW | >=2008 |

- When unit-specific data are available, we use that data for those units.  When unit-specific data are not available, we use generic assumptions associated with the appropriate bucket.

- California Energy Commission paper “The Use of Heat Rates in Production Cost Modeling and Market Modeling” was the source of unit-specific data for some units.  See Table 1.

  - Publicly available information

  - Includes incremental heat rate data on 66 generating units in CA

  - The incremental heat rate data for these units are entered into the database for those specific units

  - For the buckets which contain units with data in the CEC paper, a CA unit was chosen as the generic unit for that bucket

    - This unit has approximately the average size and the average vintage of all the units from the CEC paper that fall into that bucket

      - The Platts database was used to develop generic assumptions which were applied to units which did not have publicly available unit-specific data.  See Table 2.

        - Database includes incremental heat rate data for some but not all units

        - For buckets which aren’t assigned a generic unit from the CEC paper, a unit is chosen from the Platts database to be the generic unit for each bucket

          - There is sometimes sparse Platts incremental heat rate data among the units in a bucket

          - The unit chosen as the generic for that bucket has no missing incremental heat rate data in Platts and has an annual average heat rate closer to the SSG-WI assumption for that bucket than any other plants in that bucket

          - Some buckets have no units with incremental heat rate data in Platts.  In this case, the generic incremental heat rate of another bucket with similar characteristics is used for that bucket

- Coal, geothermal, nuclear, and solar units are treated as baseload units and are assigned annual average heat rates, but not incremental heat rates

- Generic assumptions other than incremental heat rates for thermal unit commitment are seen in Table 3.